## Slide 1
POWER BANK
User Manual Mod.T113S
Magnetic wireless Solar Power bank
Solar charging is only an emergency charging method, and the efficiency of solar
panels is constrained by natural conditions such as day and night, seasons,
geographic latitude, altitude, as well as random factors like clear or cloudy
weather, rain, etc. Please do not rely on solar energy as the primary means of
charging. For everyday use, kindly use the charging cable provided by us and
charge the product through the adapter.

## Slide 2
■ Product Specification:
● Model No.: T113S
● Battery Type: Rechargeable Lithium-ion Polymer Cell
● Solar Charging Input:5.5V/100mA
● Input(Type-C): 5V⎓2A; 9V⎓2A; 2V⎓1.5A; (PD18W Max)
● Output(USB-A): 5V⎓3A; 9V⎓2A; 12V⎓1.5A; 5V⎓4.5A; (SCP22.5W Max)
● Output(Type-C): 5V⎓3A; 9V⎓2.22A; 12V⎓1.66A; (PD20W Max)
● Output (Wireless charging): 5W; 10W; 15W; (15W Max)
● Charging Time: About 3-4 hours to fill up (using PD18W charger)
● Working Temperature: 0°C-50°C
● Product Size: (L)108×(W)69×(H)22(mm)
● Product Weight: ≈207g
■ Schematic:
① Output(USB-A) ② Input/Output（Type-C） ③ LED battery capacity indicator
④ Fast Charge Indicator ⑤ Switch button ⑥ Wireless discharge area
⑦ Solar Panel

## Slide 3
2. Store electricity in this mobile power supply
(1) Charge the power bank through power adapter
Choose a regular charging cable, connect the corresponding connector to the
corresponding input port of this product, and connect the USB connector to the power
adapter of your mobile phone. The LED indicator light flashes during charging. After full
charging, the 4 LED power indicator lights are always on. Please stop. Power digital devices
(2) Charge the power bank through sunlight
Put the power bank's solar panel under the sunlight's vertical irradiation or sunny
environment (Avoid high temperature, battery may damaged under high temperature
condition), the power bank will charge itself by absorbing the sunlight, the solar charging
indicator become green at this moment, that means the power banks is being charged by
sunlight.
■ Instructions for use :
1. A single short press of the switch displays the remaining power of the mobile
power supply.
The 4 LED power indicators respectively indicate the battery capacity status as follows:
⚠ Precautions:
If you find any undesirable phenomena such as bulging or
leakage of the product during use, please stop using it immediately.

## Slide 4
3. This mobile power supply charges digital devices
Check whether the charging voltage of digital products matches the output voltage of this
mobile power supply.
(1) Power supply for mobile phones, tablets and other digital devices
Use the built-in cable or output port of this mobile power supply to charge digital products.
The LED indicator light will light up. When the digital products are fully charged, please stop
supplying power to the digital devices.

## Slide 5
(2) Power supply for wirelessly charged digital devices
Correctly place the digital product that supports wireless charging in the magnetic wireless
charging area, and fit it closely with the digital product to automatically enter the charging
state . When the digital product is fully charged, please stop powering the digital device.
⚠ Note:
●This wireless charger is not compatible with non-Magsafe phone cases, such as Otterbox
Defender phone cases.
●Do not use adapters with outputs below 5V/1A (5W).
●Using wireless chargers to charge is more convenient than using wired chargers, but is
limited by current wireless technology. Therefore, charging speed is slower than wired
chargers.
●High temperature will reduce the charging speed and limit the power. This is a problem
that occurs with all wireless chargers. It is recommended to charge the device in an
environment with a temperature below 25℃/77℉.
●The position of the mobile phone protective case and the device on the wireless charger
will affect the charging speed. The further away from the center of the wireless charger, the
slower the charging speed.
⚠ Notice:
When the power of this mobile power supply is too low, the battery indicator light flashes
and the power output is disabled.

## Slide 6
■ Important safety instructions:
When using this product, it is important to take basic precautions, including:
●Store this product in a cool and dry place.
●Do not store this product in a high temperature or humid environment.
●Using a power supply or charger not recommended or sold by the manufacturer of this
product may result in a risk of fire or personal injury.
●Operating temperature should be between 32 to 104°F (0 to 40°C).
●Do not disassemble the product. If this product requires service or repair, please see
qualified repair personnel. Improper reassembly may result in risk of fire or personal
injury.
●If this product is not used for a long time, it should be charged and discharged every
three months.
●This product may generate heat while charging. This is normal and nothing to worry
about.
●Under normal operating conditions, battery performance will gradually decline over
several years.
●Do not expose the product to fire or high temperature.
●Do not use harmful chemicals or detergents to clean this product.
●Improper use, dropping or excessive force may cause damage to this product.
●When disposing of used batteries, please separate batteries with different
electrochemical systems.
●Please note that a discharged battery may cause fire or smoke.
●Caution: There is a risk of explosion if the battery is replaced with the wrong type.
●Warning: Batteries (battery pack or installed) must not be exposed to excessive heat,
such as sunlight or fire.
●The battery may explode or leak flammable liquid or gas under extremely low pressure.
⚠ Warning:
Use this product in accordance with the enclosed instructions. Ignoring the
instructions may cause the product to catch fire or other damage. Keep this
product out of the reach of children.
This symbol means that the product must not be disposed
of as domestic waste, and should be handed over to an
appropriate collection center for recycling.
Proper disposal and recycling help protect natural
resources, human health and the environment. Contact
the local municipality for more information on how to dispose of and
recycle this product.